## Slide 1
Cognitive workload analysis of Control Room Operators using Electroencephalography(EEG) and Eye-tracking
Dr. Mohd Umair Iqbal
Research Associate
Department of Industrial and Systems Engineering
University of Wisconsin Madison
(mohammadumai@wisc.edu)
Dated: April 16, 2024. Tuesday

## Slide 2: Safety in olden days
Nitroglycerine manufacture: Dangerous
Hazard: Wrong composition
Task:
  Continuously watch a thermometer
  Open a valve quickly to dump the whole batch to prevent an explosion
https://www.austehc.unimelb.edu.au/tia/610_image.html
One-legged Stool!

## Slide 3: Human Factors
Human factors (HF) is a scientific discipline that is concerned with the
  understanding of interactions of people with other elements of the work system
  in order to optimize their well-being and overall system performance (IEA Council, 2019)
IEA. (2021). Definitions, Domains of Specialization, Systemic Approach. https://iea.cc/definition-and-domains-of-ergonomics/
Fig. A basic representation of human factors
Top ten key issues in hazardous industries (HSE, 2022):
Managing Human Error
Training and Competence
Workload
…
HSE (2022b). Introducing key topics. https://www.hse.gov.uk/humanfactors/top-ten.htm
Notes: In the context of highly hazardous industries, the UK Health and Safety Executive identified the top issues as human failures, HF in design, procedures, organizational culture, organizational change, staffing, training and competence, safety-critical communications, fatigue and shift work, and finally, maintenance, inspection, and testing. The application of HF principles can help minimize risk. The reader is referred to HSE (2022b) for more details.

## Slide 4: Nature of Human-Machine Interaction
Fig. A typical industrial control room
Increasing complexity
Digitalization
Automation
Abundance of information
Shift in role
Operator often out of loop with the system

## Slide 5: Mental Models are critical for smooth operation
Mental Models:
  Mapping of the properties of the task to its representation in the mind of the operator (Rasmussen, 1982, Moray, 1988).
Rasmussen, J., (1986). Information Processing and Human-Machine Interaction: an Approach to Cognitive Engineering. North-Holland, Amsterdam.
Moray, N., Lootsteen, P., & Pajak, J. (1986). Acquisition of process control skills. IEEE Transactions on Systems, Man, and Cybernetics, 16(4), 497-504.
Perception
Inputs
Output
Interpretation
Reaction
Feedback
Internal Feedback
Difficulties in Perception, interpretation and reaction can increase cognitive workload
and lead to mis-operation
Need for highly skilled operators and advanced performance assessment
Notes: Casual Relationships within an equipment
Across equipment due to mass and energy balances
Due to Control structure
Need to operate in agile fashion to capture market and supply chain dynamics

## Slide 6: Traditional Performance Assessment
Operator’s performance is assessed primarily in terms of:
  Number of successes and failures
  Response times
  Deviation of operator actions from predefined sequence
  Expert judgement
Cognitive aspects of performance often ignored
Eye-tracking and EEG
  Insights into cognitive aspects of performance

## Slide 7: Eye-tracking
Technique for monitoring the movements of the eyes of a person
Based on eye-mind hypothesis
  Movement of eyes serves as a trace of attention allocation (Just and Carpenter, 1980)
Typical measurements:
  Coordinates of gaze position
  Diameter of pupil (pupillometry)
Just, M. A., & Carpenter, P. A. (1980). A theory of reading: From eye fixations to comprehension. Psychological review, 87(4), 329.

## Slide 8: Eye Gaze Movement
210
227
213
236
255
280
262
Fixation: Period during which the eye is relatively still (200-300 ms)
Saccade: Quick eye movements between fixations (30-80 ms)
Peak saccadic velocity: Highest velocity reached during a saccade
time
Velocity

## Slide 9: Eye tracking based insights
Bhavsar, P., Srinivasan, B., & Srinivasan, R. (2016). Pupillometry based real-time monitoring of operator’s cognitive workload to prevent human error during abnormal situations.
Sharma, C., Bhavsar, P., Srinivasan, B., & Srinivasan, R. (2016). Eye gaze movement studies of control room operators: A novel approach to improve process safety.
Bhavsar, P., Srinivasan, B., & Srinivasan, R. (2017). Quantifying situation awareness of control room operators using eye-gaze behavior.
Das, L., Iqbal, M. U., Bhavsar, P., Srinivasan, B., & Srinivasan, R. (2018). Toward preventing accidents in process industries by inferring the cognitive state of control room operators through eye tracking.
Pupil diameter is a marker of control room operator’s workload (Bhavsar et al., 2016)
Eye gaze pattern of some participants who are successful in controlling a disturbance resemble failure groups (Sharma et al., 2016)
Eye gaze entropy can differentiate expert and novice operators (Bhavsar et al., 2017)
Eye tracking metrics such as fixation duration and saccade duration can reveal information about evolution of cognitive states (Das et al., 2018)

## Slide 10: Entropy: A measure of Learning
An eye-tracking based study

## Slide 11: Experimental Protocol
Experimental subjects:
  5 graduate students of chemical engineering
Instructions
  Instruction manual and video on how to operate the plant.
Task
  Bring the process variables to within acceptable limits if a disturbance occurred
Fig. HMI of the ethanol process with which the operators interact

## Slide 12: Typical Task
Operator monitors the process
Alarm gets triggered to alert the operator
Operator takes action in terms of slider movement
Scenario completion or shutdown
Fig. 5: Slider position trend with time

## Slide 13: Nature of the tasks
Task No. | Disturbance | Corrective Action
1 | Coolant flow rate | Move coolant slider to appropriate position
2 | Coolant flow rate and coolant valve getting stuck | Identify bypass valve, and use it to maintain coolant flow rate

## Slide 14: Entropy: First alarm to first slider action
Chart: Entropy from first alarm to first slider action
Task 1 | 0 | 0.18764 | 0 | 0.08609 | 0.071429
Task 2 | 0.08609 | 0.21479 | 0.32076 | 0.13 | 0.068872
Fig. Comparative gaze entropy for different participants from first alarm to first slider action
Increase in entropy reflects exploration by the operators to find an alternative to the stuck valve
Notes: Tries to find an alternative when slider gets stuck during task 2, that results in increase in entropy

## Slide 15: Entropy: First slider to last slider action
Chart: Entropy from first slider to last slider action
Task 1 | 0 | 0.11479 | 0.37829 | 0.30257 | 0.3498
Task 2 | 0 | 0.1 | 0.17857 | 0.23244 | 0
Fig. Comparative gaze entropy for different participants from first slider to last slider action
Once the slider is identified, operator knows the effect of moving the slider and doesn’t look at other sliders. Hence entropy decreases during the second repetitive task.
Notes: Once the slider is identified, operator knows the effect of moving the slider and doesn’t look at other sliders. Hence entropy decreases during the second repetitive task.

## Slide 16: Summary
Decrease in entropy
  Reflects learning of a participant
  Change in mental state : ‘more entropy’ to ‘less entropy’
Decrease in cognitive workload
  Relative relief of the working memory load due to compensation from prior belief/learning
Notes: (Joseph, 2013)

## Slide 17
Electroencephalography (EEG)
EEG is the recording of the electrical activity (in microvolts) on the scalp, by placement of electrodes/sensors
17
Fig. An operator wearing an EEG device
Fig. A sample of raw EEG data
EEG signal is often analysed in frequency domain
Commonly analysed bands:
  Delta(1- 3Hz), Theta (4- 7 Hz), Alpha(8- 13 Hz), Beta (14- 30 Hz)
Fig. A single electrode EEG device (Neurosky)
http://neurosky.com/

## Slide 18: Dynamic assessment of mental model mismatches and cognitive workload
Based on the power spectral density of Theta band (4 – 7 Hz)

## Slide 19: Methodology

## Slide 20: Illustrative Example 1
Decrease in theta power spectral density indicates mental model-process behaviour match

## Slide 21: Illustrative Example 2
Increase in theta power spectral density indicates mental model-process behaviour mismatch

## Slide 22: Summary
Delta power spectral density can capture cognitive workload changes during a task
High values of delta power spectral density represent high workload
Identify high workload instances/tasks

## Slide 23: Training assessment using EEG
A clustering based approach based on power spectral densities in the range of
1-30 Hz

## Slide 24: Experimental Study
Fig. HMI of the ethanol production plant
Trials: 7-8 trials performed by each participant resulting in a total of 438 tasks

## Slide 25: Schematic of the Methodology
Fig. Simplified proposed methodology
Fraction of time during which operator is in
low power cluster
High
Low
Poor cognitive performance
Better cognitive performance

## Slide 26: Illustrative Example 1
Fig. Operator behaviour and alarm occurrences during different trials.
Operator uses multiple sliders reflecting the inability to understand the process behaviour, and it results in failure
Tries multiple sliders initially but identifies the correct slider towards the end, still fails
Learns the direction of the correct slider, and succeeds to clear all the alarms
Operator resorts to the smooth movement of the slider, and takes lesser time (45s) to clear the alarm, thus showing expert behavior

## Slide 27: Process and Behavioural Metrics
Fig. Process and behavioural metrics during different trials of an operator

## Slide 28: Cognitive Metric
is lower for failure trials compared to successful trials
Difference in cluster fraction (, time (and integral absolute abnormality () also show improvement
Increase in low energy cluster fraction represents decrease in cognitive workload
Decrease in cognitive workload reflects improvement in cognitive performance

## Slide 29: Illustrative Example 2
Operator uses two sliders reflecting the difficulty in understanding the process behaviour, but somehow manages to clear all alarms
Operator starts with the correct slider but moves it in wrong direction initially, and then also plays with another slider
Operator uses the correct slider to clear the alarm, but has he really learned?
Operator starts with the correct slider but moves it in wrong direction, and then resorts to the use of multiple sliders
Fails to clear the alarms which he had cleared in previous trials
Fig. Operator behaviour and alarm occurrences during different trials.

## Slide 30: Cognitive Metric
From trials 3 to 5, the operator clears all the alarms, but his cognitive workload is still increasing (as reflected by decrease in )
In trial 6, the operator surprisingly fails, reflecting possible absence of complete learning during the previous trials
High energy cluster fraction can capture absence of learning

## Slide 31: Summary
Advanced Training assessment for improved safety
Paves way for designing individual-centric training programs
Operator training
Cognitive behavior based data analytics
Instructor/automated system
Physiological measurement
Novice operator
Skilled operators

## Slide 32: Multi-class classification of control room operators’ cognitive workload using the fusion of eye-tracking and electroencephalography
A machine learning based approach to estimate cognitive workload of operators at three levels

## Slide 33: Proposed Methodology

## Slide 34: Basis for Cognitive workload labels
Control room operator tasks are highly dynamic, and the perception of cognitive workload is highly challenging
Feedback-based cognitive workload assessment is prone to bias
Integral absolute abnormality (IAA)
  Measures the deviation of process variables from alarm limits over a time period
  High IAA often associated with failure to control an abnormality
  IAA decreases with increase in expertise (Iqbal et al., 2021, Shahab et al., 2022)
Iqbal, M. U., Shahab, M. A., Choudhary, M., Srinivasan, B., & Srinivasan, R. (2021). Electroencephalography (EEG) based cognitive measures for evaluating the effectiveness of operator training. PSEP.
Shahab, M. A., Iqbal, M. U., Srinivasan, B., & Srinivasan, R. (2021). Metrics for objectively assessing operator training using eye gaze patterns. PSEP.

## Slide 35: Summary of Feature Categories
S. NO. | Feature Category | Feature Description
1 | Pupil | P1: PSD of pupil diameter signal in the range of 0 – 0.5Hz P2: PSD of pupil diameter signal in the range of 0.5 – 1 Hz P3: PSD of pupil diameter signal in the range of 1 – 1.5 Hz P4: PSD of pupil diameter signal in the range of 1.5 – 2 Hz P5: Average pupil diameter
2 | EEG | δ: PSD of EEG signal in the range of 1 – 3 Hz θ: PSD of EEG signal in the range of 4 – 7 Hz α: PSD of EEG signal in the range of 8 – 13 Hz β1: PSD of EEG signal in the range of 14 – 20 Hz β2: PSD of EEG signal in the range of 21– 30 Hz
3 | Gaze | G1: Longest Fixation duration/shortest Fixation duration G2: Normalized Fixation Number, i.e., No. of fixations/time G3: Normalized Fixation Duration: Total fixation duration/time G4: Standard deviation of fixation duration G5: Mean of fixation duration

## Slide 36: Decision Trees: Pupil, EEG and Gaze Based
Fig. a) Decision tree for operator O4 trained using a) pupil-based features b) EEG based features c) Gaze based features
1- Low cognitive workload 2- Medium cognitive workload
3- High cognitive workload
Fig. a) Confusion matrices for three levels of cognitive workload obtained using a) pupil-based features b) EEG based features c) Gaze based features

## Slide 37: Fusion of Features
Fig. Decision tree for operator O4 trained on the fusion of pupil, EEG, and gaze-based features
1- Low cognitive workload 2- Medium cognitive workload
3- High cognitive workload
Fig. a) Confusion matrices for three levels of cognitive workload obtained using fusion of pupil-based, EEG-based and gaze based features

## Slide 38: Result Summary
S. NO. | Feature Combination | Overall accuracy (%)
1 | Pupil only | 60.87
2 | EEG only | 45.65
3 | Gaze only | 50.00
4 | Pupil + EEG | 63.04
5 | Pupil + Gaze | 65.22
6 | EEG + Gaze | 39.13
7 | Pupil +EEG + Gaze | 69.56
Operator O4: Fusion of features results in increase in accuracy of workload classification
Aygun et al. (2022) report a three-level cognitive workload mean classification accuracy of 51.59% using pupil-based features in a driving task.
Braarud et al. (2020) report a workload classification accuracy of 63% based on speech features. (Nuclear domain)

## Slide 39: Population Model
S. NO. | Feature Combination | Overall accuracy (%)
1 | Pupil only | 54.35
2 | EEG only | 50.20
3 | Gaze only | 50.62
4 | Pupil + EEG | 63.90
5 | Pupil + Gaze | 63.07
6 | EEG + Gaze | 52.28
7 | Pupil +EEG + Gaze | 66.80
Fig. Confusion matrices for population-level decision trees trained using all features for 3-level workload classification
Braarud et al. (2021) have reported a mean accuracy of 59% for a generalized model of workload that can be applied to nuclear power plant operators.
Fusion of sensors improves cognitive workload classification accuracies at population level
1- Low cognitive workload 2- Medium cognitive workload
3- High cognitive workload
Notes: Braarud, P. Ø., Bodal, T., Hulsund, J. E., Louka, M. N., Nihlwing, C., Nystad, E., ... & Wingstedt, E. (2021). An investigation of speech features, plant system Alarms, and operator–system interaction for the classification of operator cognitive workload during dynamic work. Human factors, 63(5), 736-756.

## Slide 40: Fusion improves class-wise accuracies
Label Category (Workload Class) | Pupil Only (%) | EEG Only (%) | Gaze Only (%) | Pupil + EEG (%) | Pupil + Gaze (%) | EEG + Gaze (%) | Pupil + EEG + Gaze (%)
1 | 64.4 | 55.4 | 47.5 | 67.3 | 70.3 | 51.5 | 70.3
2 | 54.0 | 54.0 | 53.0 | 62.0 | 59.0 | 52.0 | 66.0
3 | 30.0 | 27.5 | 52.5 | 60.0 | 55.0 | 55.0 | 60.0
Table . Population-level model accuracies for multi-level workload classification (Class-wise)

## Slide 41: Conclusions
Cognitive demands are more relevant than ever
  Push towards digitalization and automation
  Advent of Industry 5.0
Fusion of different variety of features results in an increase in cognitive workload classification accuracy
  Reflects advances in cognitive performance assessment
  Can be used to develop sophisticated training assessment platforms for process industry
Improved assessment translates to improved safety
Current work has the potential to guide application of human factors in process industries

## Slide 42: Future Work
Integrate multiple sensors for more robust performance evaluation
  Different sensors capture different aspects of cognitive workload. For instance, Eye tracking (visual aspects of workload), EEG (Neural aspects)
Identify and evaluate precursors to sub-optimal performance which include fatigue and engagement levels
  Relevant during long-working hours
Evaluate and improve HMI design for enhancing the efficiency of interaction between operators and machines
Understand dynamic Human-Machine collaboration

## Slide 43: Future Work Contd…
Develop adaptive training protocols based on mental state of operators
  Adaptive training increases pace of learning (Chaouachi et al., 2019)
Study cognitive workload during team interactions
Develop cognitively aware computing systems for communicating user state
Evaluate the effectiveness of virtual reality based training (Srinivasan et al., 2022)
Develop systematic methodology to guide human factor specialists
Chaouachi, M., Jraidi, I., Lajoie, S. P., & Frasson, C. (2019). Enhancing the learning experience using real-time cognitive evaluation. International Journal of Information and Education Technology, 9(10), 678-688.
Srinivasan, B., Iqbal, M. U., Shahab, M. A., & Srinivasan, R. (2022). Review of virtual reality (VR) applications to enhance chemical safety: from students to plant operators. ACS Chemical Health & Safety.

## Slide 44: Big Picture
Srinivasan, R., Srinivasan, B., & Iqbal, M. U. (2022). Human factors in digitalized process operations. MCPS
Aviation
Driving
Health care
Space Exploration
Virtual/ Augmented Reality
Human-Robot Interaction
Marine
Construction

## Slide 45: Future Work- Pictographic view
Comfort, experience, sense of presence and effectiveness
Virtual Reality (VR)/ AR
Multi modal fusion
Human Robot Collaboration
Allocation of tasks
Trust between man and machine

## Slide 46: References
The presentation is based on the following studies:
Iqbal, M. U., Srinivasan, B., & Srinivasan, R. (2018). Towards obviating human errors in real-time through eye tracking. In Computer Aided Chemical Engineering (Vol. 43, pp. 1189-1194). Elsevier.
Iqbal, M. U., Srinivasan, B., & Srinivasan, R. (2020). Dynamic assessment of control room operator's cognitive workload using Electroencephalography (EEG). Computers & Chemical Engineering.
Iqbal, M. U., Shahab, M.A., Chowdhary, M., Srinivasan, B., & Srinivasan, R. (2021). Electroencephalography (EEG) based Cognitive Measures for Evaluating the Effectiveness of Operator Training. Process Safety and Environmental Protection.
Iqbal, M. U., Srinivasan, B., & Srinivasan, R. (2023). Multi-class classification of control room operators’ cognitive workload using the fusion of eye-tracking and electroencephalography. Computers & Chemical Engineering.
Srinivasan, R., Srinivasan, B., & Iqbal, M. U. (2022). Human factors in digitalized process operations. MCPS

## Slide 47: Acknowledgement
Prof. Rajagopalan Srinivasan
Chemical Engineering
IIT Madras
Head, DART Lab
Prof. Babji Srinivasan
Applied Mechanics and Biomedical Engineering
IIT Madras
Core Faculty, DART Lab
American Express Lab for Data Analytics, Risk and Technology, IIT Madras
Colleagues: Dr. Mohammad Aatif Shahab, Mahindra Choudhary

## Slide 48: We cannot improve what we cannot measure
Questions?
Thank you